## Slide 1
EmotiFi
Privacy-Preserving Contactless
Emotion Recognition
using Wi-Fi CSI & Deep Learning
Edge AI
Wi-Fi Sensing
On-Device Inference
Privacy-Safe
Sabir Jan
BS Computer Engineering — COMSATS University Islamabad
Final Year Project
Live CSI Spectrogram

## Slide 2
Problem Statement
📷 Cameras
Privacy violations, poor low-light performance, intrusive surveillance
⌚ Wearables
Uncomfortable, require consent, impractical for passive monitoring
🧪 Lab Sensors
Expensive, require specialist setup, not scalable
We Need A System That Is...
✅ Contactless
✅ Privacy-Preserving
✅ Real-Time
✅ Low-Cost
✅ Camera-Free
"Works in darkness. Through walls. Without a camera."

## Slide 3
Proposed Solution
EmotiFi uses Wi-Fi Channel State Information (CSI) captured via ESP32 to detect subtle body disturbances caused by human emotions — no camera, no wearable.
1
Capture CSI signals via ESP32
2
Convert to spectrograms
3
Apply CNN inference (ResNet18 / EfficientNetV2B0)
4
Predict emotion in real-time on Android
😄 Happy
😢 Sad
😨 Fear
😐 Neutral
😲 Surprised
Real-time prediction on Android

## Slide 4
Methodology / Approach
📡 Data Acquisition
▸ ESP32 TX sends Wi-Fi packets
▸ ESP32 RX captures CSI values
▸ USB Serial to Android
⚙️ Signal Processing
▸ Amplitude extraction
▸ Noise filtering
▸ Log normalization
▸ Spectrogram generation
🧠 AI Pipeline
▸ Spectrograms → CNN
▸ ResNet18 / EfficientNetV2B0
▸ PyTorch Mobile Lite
📱 Output
▸ Real-time prediction
▸ Live spectrogram view
▸ CSV dataset logging
Wi-Fi CSI → Amplitude Extraction → Filtering → Spectrogram → CNN → Emotion

## Slide 5
Current Development Stage
✓
ESP32 TX/RX communication established
✓
Real-time CSI capture working
✓
Android USB Serial integration completed
✓
Live spectrogram rendering implemented
✓
CSV dataset generation pipeline ready
✓
PyTorch Lite model integrated
✓
Real-time mobile inference pipeline under testing
✓
Live dashboard / web communication prototype available

## Slide 6
System Architecture
ESP32
Transmitter
Wi-Fi TX
ESP32
Receiver
CSI Capture
Android
App
USB Serial
Signal
Preprocessing
Filtering
Spectrogram
Generator
FFT-based
CNN Model
(ResNet18)
PyTorch Lite
Emotion
Prediction
Real-time
Real-time
Contactless
Privacy-safe
Edge AI
No Cloud
Live CSI data stream from ESP32 receiver

## Slide 7
Tools & Technologies
🔧 Hardware
▸ ESP32 (TX & RX)
▸ USB OTG Cable
▸ Android Phone
▸ 802.11n Wi-Fi
💻 Software
▸ Android Studio
▸ Java
▸ Python
▸ Node.js
▸ React
🧠 AI / ML
▸ ResNet18
▸ EfficientNetV2B0
▸ PyTorch Mobile Lite
▸ ONNX Runtime
📊 Signal Processing
▸ FFT Spectrograms
▸ CSI Amplitude
▸ Log Normalization
▸ Custom CSI Dataset

## Slide 8
Dataset & CSI Parameters
CSI Configuration
Wi-Fi Channel
6
Channel Bandwidth
20 MHz
CSI Sampling Rate
100 pps
Number of Subcarriers
64
Center Frequency
2.4 GHz
Sampling Time Window
5 sec
Sampling Frequency
100 Hz
Transmitter Power
20 dBm
Emotion Classes
5
Collected Dataset Summary
Class
Per Person
No Reflect.
With Reflect.
Neutral
2
60
188
Happy
2
60
188
Sad
2
60
188
Fear
2
60
188
Surprise
2
60
188
Total
10
600
940
Without Reflectors
600 total samples
Baseline setup
With Reflectors
940 total samples
Enhanced signal clarity
Two-approach dataset: reflectors boosted signal quality and increased class-separability in spectrograms.

## Slide 9
Model Training
Experiment 1 — ResNet18 on RGB Spectrograms
Why ResNet18?
▸ Fast, efficient deep learning model for image classification
▸ Skip connections help learn better even in deep networks
▸ Good starting point for learning emotional signal patterns
▸ Lightweight enough for PyTorch Mobile deployment
⚠ Problem: Test Accuracy Only 49%
Model overfit on training data — poor generalization to new subjects.
Root Causes Identified
▸ Data leakage — subject identity leaked across train/test splits
▸ Noisy spectrograms with overlapping emotional signals
▸ Unclear emotion patterns in raw CSI data
Training accuracy ~98% vs Test 49% — classic overfitting

## Slide 10
Model Training
Experiment 2 — EfficientNetV2B0 + Slicing & Augmentation
Why Switch to EfficientNetV2B0?
ResNet18 overfit and failed on new data. EfficientNetV2B0 balances width, depth, and resolution — better generalization with same compute budget.
Improvements Applied
▸ Spectrogram slicing — improve feature visibility
▸ Data augmentation — increase training diversity
▸ Without augmentation: Test Acc = 29%
▸ With augmentation: Test Acc = 34%
Still insufficient — gap between train & test accuracy remains large.
Left: slicing only (29%). Right: slicing + augmentation (34%)

## Slide 11
Model Training
Experiment 3 — Absolute Difference Spectrograms + Fair Data Splitting
What Changed in Exp. 3?
▸ Absolute Difference spectrograms — isolate emotional signal changes more clearly
▸ Improved data split — all 5 emotions per person kept in same split to prevent data leakage
▸ Result: better separation of emotional signals, model learns meaningful patterns
With Augmentation
Test Acc: 44.0%
Without Augmentation
Test Acc: 42.4%
Key Fix: Data Leakage Prevention
Before: Random split → same person's samples in both train & test
Now: All 5 emotions per person stay in ONE split — fair evaluation on truly unseen subjects
Exp 3 training curves — improved generalization with absolute difference input

## Slide 12
Model Training
Breakthrough — Reflector Spectrograms Push Accuracy to 90%+
❌
Used Spectrograms
Basic approach
→
📡
Added Reflectors
Better signal clarity
→
🎨
Full RGB Images
Preserved emotion signatures
→
🔀
Random Data Split
Fair evaluation
→
🔍
Tracked Mistakes
Deeper insights
What Changed
Before
After
Problem Fixed
Sliced Images
Full RGB Images
Distorted augmentations
Separate CSVs
Unified Dataset
Risked data overlap
No Error Tracking
Tracked Mistakes
Overlooked model errors
Random Splits
Person-wise Splits
Caused data leakage
Train/Val/Test accuracy reaching 90%+ with reflector spectrograms
🏆 Best Result
Test Accuracy: 90%+
Reflectors + Full RGB + Person-wise splits
Misclassification analysis → further insights

## Slide 13
Live Spectrogram Visualization
Initial CSI Spectrogram
(Blue palette — quiet state)
Current Spectrogram
(Active CSI with warm signal)
Debug View
(High-energy signal detected)

## Slide 14
Real-Time Emotion Inference
Three test runs: Fear 70% | Surprised 78% | Happy 73.83%
Detailed output with raw logits
⚠️ Note: '334.98% confidence' is a known softmax display bug — raw logits are being used directly. Fix in progress (apply softmax before percentage display).

## Slide 15
Expected Impact & Use Cases
🏥
Healthcare
Mental wellness monitoring, stress & anxiety detection in clinical settings
🏠
Smart Homes
Emotion-aware environments that adapt lighting, music, and ambiance
👴
Elderly Care
Non-intrusive continuous monitoring without cameras or wearables
💻
HCI
Emotion-adaptive interfaces for gaming, education, and productivity apps
🔒
Security
Works in darkness, through obstacles, with zero privacy footprint
🌐
IoT
Embedded into existing Wi-Fi infrastructure — no new hardware needed

## Slide 16
EmotiFi
Privacy-Preserving · Contactless · Real-Time · On-Device
Wi-Fi Sensing
No cameras needed
Edge AI
On-device inference
Real-Time
Low latency pipeline
Custom Dataset
Original CSI data
Embedded AI
PyTorch Mobile Lite
The Full Pipeline
Wi-Fi CSI → Amplitude Extraction → Filtering & Normalization → Spectrogram Encoding → CNN Feature Learning → Emotion Classification → Mobile Real-Time Inference
Sabir Jan | BS Computer Engineering | COMSATS University Islamabad | Final Year Project
github.com/Saber7Jan/EmotiFi